## Slide 1: EVPN a very short introduction

## Slide 2: Acquiring MAC tables
Ethernet MAC addresses are arbitrary identifiers – not locators
how does an Ethernet switch learn how to forward?
802.1D STP and learning+flooding+aging
MEF switch – ignore MAC addresses
  and NMS configures VLAN tags
TRILL (RFC 6326) – shortest-path-bridging (Dijkstra) using IS-IS
SDN – centrally located God Box configures entire network
  using protocol such as OpenFlow or Yang
EVPN (RFC 7432) – distributes MAC addresses via BGP
  driven by operational needs

## Slide 3: Ethernet VPNs
Ethernet VPNs connect customer sites at the Ethernet layer
but not necessarily over Ethernet networks
PBBN (MAC-in-MAC) uses a pure Ethernet backbone network
but without learning/flooding (if NMS setup called PBB-TE)
L2VPN (VPWS/VPLS) uses Ethernet PW over MPLS networks
EVPN may use
  MPLS PWs
  VXLAN over UDP over IP
  new tunneling mechanisms, such as :
    Geneve = Generic Network Virtualization Encapsulation)
    NVGRE = Network Virtualization using GRE

## Slide 4: DCI Use case
EVPN addressed the Data Center Interconnect (DCI) use case
DCI intelligently connects data centers, enabling
inter-DC workload migration (AKA VM mobility)
Global Server Load Balancing (AKA server clustering)
business continuity across failures
Servers in different DCs are not on the same IP subnet
so identity continuity and basic connectivity
is usually guaranteed using MAC addresses
When a VM spins up it is allocated a MAC address
and if migrated this address remains unchanged
But there may be 100s of thousands of MAC addresses per DC!
migrating huge numbers would cause massive ARP storms
and necessitate colossal relearning procedures

## Slide 5: EVPN as SDN mechanism
How is EVPN different from L2VPN (VPWS, VPLS)?
L2VPNs use Ethernet PWs for transport
but otherwise rely on standard Ethernet techniques, e.g.,
802.1D learning/flooding/aging
split horizon instead of STP
ARP to associate MAC and IP addresses
EVPN configures MAC tables SDN-style
although it happens to use BGP rather than an SDN SBI
(since it was invented by Yakov Rekhter – one of the authors of BGP!)
This makes EVPN ideal for DCI
although it is also useful for E-LINE/E-LAN L2VPN services
and is being studied for IoT applications

## Slide 6: EVPN advantages
At least for the DCI use case
there are many advantages to configuring via control plane
instead of learning in the data plane :
faster (no aging, flooding, etc.)
faster to repair after failures
scales better (distribute thousands of MAC addresses)
allows applying policy rules
restrict how and to whom information is distributed
can isolate groups of devices (hosts, servers, VMs)
enables CE multi-homing (a CE can attach to multiple PEs)
enables CE LAG load balancing

## Slide 7: EVPN – PEs and CEs
EVPN uses BGP between PEs
  PEs advertise to other PEs :
  MAC addresses learned from connected CEs
  an MPLS label
Learning between PEs and CEs is done by the data plane
customer network
C
C
C
P
PE
P
P
CE
PE
PE
P
provider network
Ethernet
learning
EVPN
advertising

## Slide 8: BGP
BGP distributes routing information in update messages
that contain Network Layer Reachability Information
along with path attributes for the NLRI
Originally NLRI was one or more destination IP prefixes
BGP version 4 became multiprotocol (MP-BGP)
by extending NLRI to additional address families, e.g.,
unicast IPv4
unicast IPv6
labelled unicast (i.e., MPLS labels)
L3VPNs
IPv4 multicast
Each of these is defined by an AFI (Address Family Identifier)
and SAFI (Subsequent (Next Hop) Address Family Identifier)

## Slide 9: BGP for EVPN
RFC 7432 defines a new address family for EVPN
based on the previously defined L3VPN address family
EVPN enables distribution of MAC addresses
or pairs of MAC+IP addresses
Thus, EVPN can support
extending Ethernet domain across multiple DCs
VM migration maintaining MAC addresses
  but reassigning P addresses
VM migration maintaining both MAC and IP addresses
without need for triangle routing

## Slide 10: Multihoming
EVPN allows multihoming using Ethernet Segment Identifiers
CE over multiple links to a PE
CE connecting to 2 or more PEs
to maintain EVPN service in the event of :
CE to PE link failure
PE failure
some MPLS network failures
Links can be in single-active or all-active mode
BUM (Broadcast, Unknown unicast and Multicast) traffic
is limited to a single link
To prevent traffic from a DC looping back to the same DC
EVPN supports split horizon based on the ESI
CE
PE
PE
same
ESI

## Slide 11: Some more EVPN advantages
EVPN prevents ARP storms
DC edge GWs only pass known traffic
DC edge GW proxy-ARPS to all known ARP requests
and discards all unknown ARP requests
EVPN can prevent MAC flapping
after VM migration
the new MAC location needs to be learned
the old location forgotten
the first might happen faster than the second
EVPN can support multicast
using replication, or P2MP or MP2MP MPLS LSPs
EVPNs can support multiple VLANs
while maintaining VLAN isolation