## Slide 1: Real-time
DSP processing is almost always real-time
Some exceptions:
work on recordings
systems with outputs that are not signals (e.g., detections)
What is real-time ?
For a signal processing system
which inputs an input signal one value at a time
hard real-time: ALWAYS finish computing output before next input
soft real-time: finish computing output on average before next input
store input points that arrive before output ready
exploit some additional delay to output
xn
yn
CPU
XTAL
memory

## Slide 2: Example
Assume samples arrive 1000 times per second fs = 1000 Hz
then the time between samples is ts = 1 millisecond
So, for hard real-time
all of the processing of a single input sample xn
in order to produce the output sample yn
must take place in less than 1 millisecond
(before the next sample xn+1 arrives)
For soft real-time
sometimes the processing of a single input sample xn
can take longer than 1 millisecond
in which case we store the next sample xn+1
until we output the output sample yn
and then start processing xn+1

## Slide 3: DSP = Hard real-time
In DSP we will only deal with hard real-time
because we perform exactly the same computations each time
(there are no conditionals)
For example
MA filters
AR filters (or ARMA)
DFT
So, if we miss a deadline once
it doesn’t help to store the next input
since the next input will also take too much time
and the situation will only get worse and worse

## Slide 4: Real-time for multi-input
What about the DFT? We can’t perform a DFT on one sample xn
it only makes sense to perform on N samples x0, x1, x2, … xN-1 !
For a system which performs calculation on N inputs
hard real-time means that
we must finish processing all N samples x0, x1, x2, … xN-1
before the next N samples xN, xN+1, xN+2, … x2N-1 arrive!
The requirement is the same as before, but on average
That is, finishing processing of N old samples
during the time N new samples appear
means on average processing a sample in a sampling time
However, in general the processing of N samples
need not reduce to N processing stages each on 1 sample!

## Slide 5: Wrong way to process N samples
You might think that we do the following:
time 0: input x0, store in buffer, but don’t perform any processing
time 1: input x1, store in buffer, but don’t perform any processing
…
time N-1: input xN-1, store in buffer
and perform all processing of N samples
before the next sample xN arrives
time N: input xN but don’t perform any processing
etc.
but that would be really hard!
We would need to process N samples in 1 sampling time
although on average we need to process 1 sample per sample time
So, what do we do instead?

## Slide 6: Double buffering
What we do is the following:
time 0: input x0 into buffer 1
time 1: input x1 into buffer 1
…
time N-1: input xN-1 into buffer 1 (filling buffer)
and start performing all processing of N samples in buffer 1
time N: input xN into buffer 2 and continue processing buffer 1
time N+1: input xN+1 into buffer 2 and continue processing buffer 1)
some time before time 2N-1: finish processing buffer 1 and output
time 2N-1: input x2N-1 into buffer 1
and start performing all processing of N samples in buffer 2
Trick:
Instead of having to swap write pointers
between buffer 1 and buffer 2
we can use a cyclic buffer
double buffer
1
2
cyclic
buffer
1
2

## Slide 7: Theorem for real-time
The computational complexity of a real-time system
that performs calculation on N inputs
must not exceed O(N)
In particular the DFT can not be performed in real-time
since
requires computing N values X0, X1, …, XN-1
each of which requires N multiplications (n = 0 … N-1)
  and is thus O(N2)
What does this theorem mean?
Why can’t we find a fast enough processor
to perform anything we want in real-time?

## Slide 8: The meaning of the theorem
Imagine that you need to program some O(N2) process
and as before samples arrive every millisecond
Let’s assume that you are told that N=1024
and that you manage to program you CPU
to finish the processing in less than 1024 milliseconds
But then it turns out that N=2048 is really needed
You now have twice the time to perform the computation – 2048 ms
but because of O(N2) you require 4 times the time – 4096 ms!
So you buy a faster processor and manage to run in real-time
but then if it turns out that N=4096 is needed
no strong enough CPU is available!
But if the complexity is O(N)
then when N is increased from 1024 to 2048
you have twice the time to perform the computation
but only need twice the time!

## Slide 9: and the solution is …
DFT and iDFT are so critical in DSP
that without a real-time implementation DSP won’t work!
The Fast Fourier Transform
reduces the O(N2) complexity of the straightforward DFT
to O(N log N)
Note we don’t need to specify the base of the log
since changing base only inserts a multiplicative constant
but we will always assume log2
But O(N log N) is higher than O(N)
and so violates the theorem that real-time requires O(N) !
O(N log N) is not low enough to guarantee real-time for all N
but is sufficiently low to enable even extremely large Ns
DSP processors are rated by
how large an FFT they can perform in real-time!

## Slide 10: Warm-up problem #1
Find minimum and maximum of N numbers x0 x1 x2 x3 ... xN-2 xN-1
minimum alone takes N comparisons prove this
maximum alone takes N comparisons prove this
So we can certainly find both with 2N comparisons
But there is a way to find both in 1½ N comparisons
x0 x1 x2 x3 ... xN-2 xN-1
smaller x0 x3 ... xN-1
larger x1 x2 ... xN-2
run over at pairs, separating into larger and smaller
– this takes ½ N comparisons
the minimum must be in the smaller list (why?)
– find it in ½ N comparisons
the maximum must be in the larger list
– find it in ½ N comparisons
altogether 3/2 N comparisons – 25% savings
Can we improve this by further decimation? Why not?
for example

## Slide 11: 2 remarks
this method uses decimation
that is separating a sequence of N elements
into two subsequences of N/2 elements
based on even and odd elements
although we reserved 2 buffers
smaller x0 x3 ... xN-1
larger x1 x2 ... xN-2
the calculation can be performed in-place
that is, without additional memory !
x0 x1 x2 x3 x4 x5 ... xN-2 xN-1
x0 x1 x3 x2 x5 x4 ... xN-2 xN-1
But to swap two values x0 x1 we do need an additional memory
y←x0 , x0←x1 , x1←y
why don’t we count this?

## Slide 12: Warm-up problem #2
Multiply two N digit numbers A and B (w.o.l.g. N binary digits)
we saw that long multiplication is a convolution
and thus takes 2N2 1-digit multiplications
But there is a faster way!
Partition the binary representation of A and B into 2 parts
A7 A6 A5 A4 A3 A2 A1 A0 = AL AR
B7 B6 B5 A4 B3 B2 B1 B0 = BL BR
Now
So partitioning factors reduces to 3/4 N2 saving 25% !
There’s a small problem here – the subtractions might add a bit!
But O(3/4 N2) = O(N2) so we haven’t changed the O complexity!

## Slide 13: Continued …
But this time we can continue
Now, 3log2(N) = Nlog23 Why is alogk(b) = blogka ?
So the complexity is O(Nlog2 3)  O(N1.585)
and O(N1.585) < O(N2) -- the O complexity has been reduced!
This is the Karatsuba (special case of Toom-Cook) algorithm
which was thought to be the fastest way to multiply
until the FFT way was discovered
3 multiplications, each N/2 bits
32 multiplications, each N/4 bits
3 log2(N) multiplications, each 1 bit
1
2
log2(N)
0
1
3
9
27

## Slide 14: Toom-Cook example
Let’s multiply A=83 times B=122 using Toom Cook
(the answer is 10,126)
A = 0 1 0 1 0 0 1 1 B = 0 1 1 1 1 0 1 0
AL = 0 1 0 1 = 5 BL = 0 1 1 1 = 7
AR = 0 0 1 1 = 3 BR = 1 0 1 0 = 10
AR =
= 5*7 *(256+16) + (5-3) * (10-7) *16 + 3*10*(16+1)
= 35 * 272 + 6 * 16 + 30 * 17
Now for ALBL we repeat the process
AL = 0 1 0 1 BL = 0 1 1 1
ALL = 0 1 = 1 BLL = 0 1 = 1
ALR = 0 1 = 1 BLR = 1 1 = 3
AL BL = 1*1*(16+4) + (1-1)*(3-1)*4 + 1*3*(4+1)
and the same for the other 2 multiplications
we then go one step further – and have 9 individual bit multiplications

## Slide 15: Decimation and Partition
The two warm-up problems had a strategy in common
If the complexity is C=cN2
then it is worthwhile to divide the input sequence into 2 subsequences
Since performing the operation on each part costs c(N/2)2 = C/4
so the two together cost C/2
If we can glue the two parts back together in less than C/2
then we have a more efficient algorithm!
But the two problems used two different methods of dividing the sequence
Decimation
x0 x2 x4 x6 EVEN
x1 x3 x5 x7 ODD
LSB sort
Partition
x0 x1 x2 x3 LEFT
x4 x5 x6 x7 RIGHT
MSB sort
x0 x1 x2 x3 x4 x5 x6 x7

## Slide 16: Radix 2
In both warm-up problems, and in the FFT algorithm we will derive
we divide up the sequence into 2 sub-sequences of length N/2
In fact we will require that N be a power of 2
so that we can continue to divide by 2 until we get to units
Such algorithms are called radix-2 FFT algorithms
We could also chose to divide it up into 3 subsequences
or 4 or 5 or any other integer into which N factors
There are special FFT algorithms for powers of other primes
and for semi-primes like N=15=5*3
In fact, only for prime N is no possibility of reducing complexity
Shmuel Winograd discovered FFTs with few multiplications
for various values of N = N1 * N2 where N1 and N2 are coprime

## Slide 17: Decimation in Time  Partition in Frequency
What does decimating a signal in the time domain
do to the frequency domain representation ?
Assume that the original signal x0 x1 x2 … xN-1
was sampled at fs
and thus by the sampling theorem
have maximum frequency fN = fs/2
Then the decimated signals, x0 x2 x4 … and x1 x3 x5 …
are sampled at fs/2
and thus have maximum frequency fs/4
So we obtain only the lower ½ of the original spectral width
in other words the LEFT partition of the spectrum
Thus DIT = PIT
We’ll see later the exact relationship between
the lower and upper partitions of the spectrum

## Slide 18: Partition in Time  Decimation in Frequency
What does partitioning a signal in the time domain
do to the frequency domain representation ?
Assume that the original signal x0 x1 x2 … xN-1
was sampled at fs and thus has duration T = N ts = N / fs
Then the partitioned signals, x0 x1 … xN/2-1 and xN/2 xN/2+2 … xN-1 have duration N/2 ts = T/2
According to the uncertainty principle
if the time duration Δt is reduced by ½
then the frequency uncertainty Δω is increased by 2
(the frequency resolution is blurred)
So, we can effectively observe only every other spectral line!
Thus PIT = DIT

## Slide 19: FFT history
The FFT has been discovered many times
perhaps as early as unpublished 1805 work by Gauss
which predates Fourier!
In 1903 Runge discovered an FFT for N a power of 2
and in 1942 Danielson and Lanczos discovered a O(N log N) DFT
However, credit is now usually given to
John Wilder Tukey – American mathematician/statistician (Princeton)
  who coined the words bit = binary digit and software
James William Cooley – American mathematician / programmer (IBM)
who published in 1965 (in order to avoid patenting)
The Cooley-Tukey algorithm is Decimation In Time
that is, it decimates the signal in the time domain
performing DFTs separately of the evens and the odds
The Sande-Tukey algorithm is Decimation in Frequency
that is, it partitions the signal in the time domain
performing DFTs separately of the 1st half and 2nd half

## Slide 20: Before starting
Recall that the DFT is
where WN is the Nth root of unity WN =
We will need three trigonometric identities
WNN = 1 (that’s the definition!)
WNN/2 = -1 (= = -1 or )
WN2 = WN/2 (= or )
They are trigonometric identities
since WN = cos() – i sin()
WN
WN
WN2 = WN/2
WNN/2

## Slide 21: DIT (Cooley-Tukey) FFT
Let’s derive the radix-2 DIT FFT algorithm!
We start by decimating the formula for the DFT
that is, we separate the even terms 2n from the odd terms 2n+1
Now, and so we can rewrite:
DFT of evens
DFT of odds
3rd identity

## Slide 22: DIT – the first step
So we have found
which shows that the DFT indeed divides up into 2 half-sized DFTs
and an additional N multiplications by (for k=0…N-1)
This is encouraging, since the glue is O(N) !
The glue factor is usually called the twiddle factor
and it is the entire difference between the contribution
of the two decimations to the original DFT
Note that we precompute and store the N twiddle factors (k=0 … N-1)
and don’t have to compute them over and over again!
Even
Odd

## Slide 23: PIF
The next step is to exploit the relationship between
  Decimation In Time and Partition In Frequency
What is the connection between
Xk in the left partition : 0 ≤ k ≤ N/2 – 1
and the corresponding component in the right partition
Xk in the right partition : N/2 ≤ k ≤ N – 1
Note that we compute exactly the same products
but add them with different signs + - + - + - + -
2nd identity
WNN/2 = -1

## Slide 24: DIT is PIF
So, we have already reduced the number of multiplications by ½
Now, the products for which (-1)n is negative are odd n
i.e., exactly those terms in the odd decimation!
So
We can draw this as a DSP diagram in a nice in-place way !
This reminds us of the N=2 butterfly
but has a twiddle factor before the butterfly
The DIF algorithm/s butterfly
has a twiddle factor after the butterfly
is the DFT sum
don’t confuse it with
(it should have an intermediate sized x …)

## Slide 25: DIT all the way
We have already saved a factor of 2 in the multiplications
but we needn't stop after splitting the original sequence in two !
Each half-length sub-sequence can be decimated again
note that this is in-place!
Assuming that N is a power of 2
we continue decimating until we get to the basic N=2 butterfly
Note that since WN/2 = WN2 we can draw this
and we only have to keep one table of

## Slide 26: Let’s continue!
Instead of explicitly writing equations for the next step
it is easier to do everything graphically
In order to make things simple, we’ll assume N=8
and explicitly draw out all the steps
  decimate the N=8 sequence into two subsequences of length 4
  decimate each of the sub-sequences of length 4
  into two sub-sub-sequences of length 2 (4 altogether)
  perform four basic N=2 butterflies
Let’s see this happen!

## Slide 27: DIT N=8 - step 0

## Slide 28: DIT N=8 - step 1
in-place!

## Slide 29: DIT N=8 - step 1 : 4 butterflies
The butterflies are all entangled – do you see them?

## Slide 30: DIT N=8 - step 2
W40 = W80
W41 = W82

## Slide 31: DIT N=8 - step 2
Note that the second stage butterflies are less entangled!

## Slide 32: DIT N=8 - step 3

## Slide 33: Complexity
An FFT of length N has
log2(N) stages of butterflies
there are ½N butterflies in each stage, each with
  1 complex multiply
  2 complex adds (1 add and 1 subtract)
So there are :
½ N log2(N) complex multiplications
N log2(N) complex additions
Which is why we say that the complexity is O(N log N)
stage 3 stage 2 stage 1
for N=8 there are 3 stages
Stage 1: 4 butterflies
Stage 2: 2*2 butterflies
Stage 3: 4*1 butterflies

## Slide 34: Well, its even a bit less
Actually, some of the multiplications are trivial!
the first stage has one trivial multiplication (=1)
the 2nd stage has 2 trivial multiplications
…
the last stage has no true multiplications (it has N=2 butterflies!)
So for N=8 there are really only 5 multiplications instead of 8log2(8) = 24 !
This is mostly important for small N!

## Slide 35: Real complexity
So far we have counted complex multiplications and additions
Each complex add entails 2 real adds
Each complex multiply is either:
4 real multiplies and 2 real adds
(a + i b) (c + i d) = (a*c – b*d) + i (a*d + b*c)
or 3 real multiplies and 5 real adds
M1 = a*c M2 = b*d M3 = (a+b)*(c+d)
(a + i b) (c + i d) = (M1 – M2) + i (M3 – M2 – M1)
So
N log2(N) complex additions = 2N log2(N) real additions
½ N log2(N) complex multiplications =
  2N log2(N) real multiplications
  and another N log2(N) real additions
  or
  3/2 N log2(N) real multiplications
  and another 5/2 N log2(N) real additions

## Slide 36: What’s going on?
Our time domain signal is not arranged x0, x1, x2, … !
The order of the input values is very strange!

## Slide 37: Bit reversal
Let’s see if we can figure it out! Here for N=16 IN-PLACE!
1st transition is cyclic left shift
2nd transition freezes the LSB and cyclic left shifts the rest
3rd transition freezes the 2 LSBs and cyclic left shifts (swaps) the rest
Altogether we find abcd  bcda  cdba  dcba
The bits of the index have been reversed !
This is called bit-reversal
  and DSP processors have a special addressing mode for it

## Slide 38: DIT N=8 with bit reversal

## Slide 39: The matrix interpretation
The FFT can be understood as a matrix decomposition
that reduces the number of operations to multiply by it
For example, when N=4
The right matrix is a permutation matrix
which carries out the bit reversal
The middle matrix comprises the butterflies
(note the block matrix form)
The left matrix is the twiddle factors

## Slide 40: What about the DIF algorithm?
The other radix-2 FFT algorithm could be called Partition in Time
but is always called Decimation In Frequency
To derive it algebraically we need to return to the DFT formula
and partition the sum into high and low halves
We then exploit that DIF to relate Xk (even k) with Xk+1
resulting in butterflies
But instead of working hard we’ll use a trick!
Performing the transposition theorem on the N=8 DIT (and a mirror reflection)
gives us the n=8 DIF!

## Slide 41: DIF N=8
DIF butterfly

## Slide 42: FIFO FFT
There are many other Fast Fourier Transform algorithms!
What if we need to update the DFT every sample?
In other words, [x0, x1, x2, … xN-1], [x1, x2, x3, … xN], [x2, x3, x4, … xN+1], …
You might already know the trick
on how to update a simple moving average
A1 = x0 + x1 + x2 + … + xN-1
A2 = x1 + x2 + x3 + … + xN = A1 – x0 + xN
A3 = x2 + x3 + x4 + … + xN+1 = A2 – x1 + xN+1
This is implemented by maintaining a FIFO of length N
adding the new input and subtracting the one to be discarded
A similar trick works for weighted MA
if the weights form a geometric progression
A1 = x0 + q x1 + q2 x2 + … + qN-1 xN-1
A2 = x1 + q x2 + q2 x3 + … + qN-1 xN = (A1 – x0)/q + qN-1 xN
A3 = x2 + q x3 + q2 x4 + … + qN-1 xN+1 = (A2 – x1)/q + qN-1 xN+1

## Slide 43: FIFO FFT (cont)
The DFT is just such a weighted moving average, with q =
but when moving from time to time we shouldn’t reset the clock!
So
and hence
requiring only 2 complex additions and one multiplication per k
or altogether N multiplications and 2N additions!

## Slide 44: Goertzel’s algorithm
Sometimes we are only interested in
the energy |Xk|2 of a few of the frequencies k
and computing all N spectral values would be wasteful
For example, when looking for energy at a few discrete frequencies
as in a DTMF detector
For such cases there is an algorithm due to Goertzel (Herzl in Russian)
which is less expensive that running many bandpass filters
The idea is to compute only the Xk needed
by using Horner’s rule for evaluating polynomials (simplify to W)
This can be further simplified to get a noncomplex recursion

## Slide 45: Goertzel 1
To make the recursion look like a convolution we use V = W-1
Changing the overall phase doesn’t change the power spectrum
which using Horner’s rule is coded like this :
Since all the xn are real, at each step Pn – Pn-1V is real
So we implicitly define a new real sequence Qn by Pn = Qn - Qn-1W

## Slide 46: Goertzel 2
After a little algebra we find the following recursion:
And the desired energy is given by
where

## Slide 47: Using Goertzel
To use Goertzel first decide on how many points N you want to use
Since Goertzel’s algorithm only works for integer digital frequencies
(that is, for analog frequencies f = k/N fs)
larger N allows finer resolution and narrower bandwidth
but also longer computation time and delay
For each frequency that is needed
compute W and A
initialize
iterate N-1 times using A
compute X using W
compute the desired squared power using A

## Slide 48: Other radixes
While radix-2 is popular, sometimes other radixes are better
The radix 4 DFT is
which corresponds to radix-4 butterflies
which is more expensive than radix-2
12 complex additions
0 true multiplications
8 complex additions
0 true multiplications

## Slide 49: FFT842
But this is only the case for N=4 itself
For powers of 4 there are only log4N = 1/2 log2N stages of butterflies
and each has ¾ N complex multiplications
and so only 3/8 log2N multiplications altogether
which is slightly less than ½ log2N !
But only half of the powers of 2 are also powers of 4
so the algorithm is less applicable …
Similarly, for N=8m there are even fewer stages
but only a quarter of the powers of 2 are powers of 8
So, the FFT842 algorithm performs as many radix-8 stages that it can
it then performs either a radix-4 or a radix-2 stage as needed
It beats out pure radix-2 algorithms on general purpose CPUs
but highly optimized radix-2 are preferable on DSPs

## Slide 50: Multiplication by FFT
When learning the Toom-Cook algorithm
we said that for large N the FFT will multiply even faster
That is because O(N log N) < O(Nlog23)
We saw that long multiplication c = a*b is actually 2N convolutions
Hence convolution in the time domain takes O(N2) multiplications
but in the frequency domain it only takes O(N)
So the strategy is instead of convolution c = a * b
use the FFT to convert from the time to the frequency domain
a→A and b→B [ O(N log N) ]
multiply point by point in the frequency domain C=AB [ O(N) ]
convert back from the frequency to the frequency domain
C → c [ O(N log N) ]
Altogether O(N log N) !

## Slide 51: Example multiplication (1)
Let’s see how this works for N=4 !
We want to multiply a = a3 a2 a1 a0 by b = b3 b2 b1 b0
We convert the numbers into time domain signals
a0 a1 a2 a3 and b0 b1 b2 b3

## Slide 52: Example multiplication (2)
For this simple case we can simply convert all 16 signals
into the frequency domain
To do this we multiply by the DFT matrix
and we find:
Of course, using the W matrix for conversion is O(N2)
But we would get the same answers with the FFT

## Slide 53: Example multiplication (3)
For example, let’s multiply 2*3
Looking this up we find is indeed S[6]
And similarly for almost all other multiplications that fit into 4 bits
0 * s = 0
1 * s = s
2 * 4 = 8
2 * 5 = 10
2 * 6 = 12
2 * 7 = 14
3 * 4 = 12
3 * 5 = 15

## Slide 54: Example multiplication (4)
All products that fit into 4 bits work correctly - except 3*3
What’s going on?
Converting back using the iDFT we find (1, 2, 1, 0)
which has a meaningless 2 bit !!!
So, we convert back into binary digits 0121
and perform the carries to get 1001 which is indeed 9
For all products that exceed 4 bits
we can use 8 bits
i.e., signals with 8 time values